## Slide 1
ELMA
by StayHere
SMS Platform Architecture
Multi-Channel · Multi-Country · High-Reliability SMS Delivery
Board Presentation | Architecture & Engineering Overview
June 2026
SMS ◆ INFRA

## Slide 2
Executive Summary
What the Elma SMS Platform does and why it matters
◆ Multi-Channel Reach
• App, USSD, and Web channels
• Unified pipeline for all entry points
• No channel-specific code paths
◆ Queue-Isolated Routing
• One queue per Country × Bank × Category
• Independent scaling per segment
• Fault containment across regions
◆ Reliable Delivery
• Persistent RabbitMQ queues (no data loss)
• Dead-letter queues for failures
• Exponential backoff retry logic
3
Entry Channels
N×N×N
Isolated Queues
2
Delivery Protocols (SMPP + SDP)
3
Deployment Tiers
0
Message Loss (Dead-letter safety)
Designed for multi-country banking operations — scalable, resilient, protocol-agnostic

## Slide 3
System Components
11 components across three deployment tiers
App Channel
Native mobile
Mobile client transactions
USSD Channel
Telecom gateway
Carrier/hosted USSD sessions
Web Channel
Browser/Cloud
Direct SMS API calls
Elma Core
C# .NET / IIS
Central transaction engine
SMS API
C# .NET / Docker
Web channel entry point
RabbitMQ Wrapper
C# .NET / Docker
Queue name resolution & publish
RabbitMQ Broker
Docker/VM
Durable message persistence
Queue Processor×N
C# Worker / Docker
One per queue — AMQP consumer
SMS Splitter GW
C# .NET / IIS
MNO routing by MSISDN prefix
MNO Passthrough
Node.js / PM2
HTTP-to-SMPP/SDP adapter per MNO
MNO SMSC
Node.js / PM2
SMPP/SDP client delivery module
Light teal = Channel / Entry | Light grey = Processing / Delivery

## Slide 4
Three Entry Channels
All converge on the same asynchronous pipeline
📱 App Channel
POST /api/transactions
• Sent to Elma Core
• Transaction validated & SMS need detected
• Enqueued asynchronously
• 202 Accepted returned immediately
• Typical triggers: OTP, balance alert, confirmation
📟 USSD Channel
POST /api/ussd/session
• Mirrors App channel exactly
• USSD response returned immediately
• SMS delivery is fully asynchronous
• No blocking of USSD session
• Same queue pipeline as App
🌐 Web Channel
POST /api/sms/send
• Hits SMS API directly (bypasses Elma Core)
• Pre-processed / external sender use-case
• SMS API → RabbitMQ Wrapper → Queue
• Independently scalable endpoint
• Suitable for bulk or direct API callers
All three channels converge on the same RabbitMQ queue pipeline — ensuring identical delivery guarantees regardless of entry point.

## Slide 5
End-to-End Message Flow
App & USSD path — 8 steps from transaction to delivery
1
Transaction Posted
▶
2
SMS Output Detected
▶
3
Queue Name Resolved
▶
4
202 Accepted Returned
▶
5
Queue Processor Consumes
▶
6
SMS Splitter Routes by MSISDN
▶
7
MNO Passthrough Delivers
▶
8
ACK Received & Msg Removed
Elma Core receives POST /api/transactions
Inspects output — OTP, alert, confirmation
Queue: {COUNTRY}_{BANK}_{CATEGORY}_SMS
HTTP client unblocked immediately
Long-lived AMQP consumer subscription
Prefix match: +25677 → Airtel Uganda
SMPP PDU or SDP HTTP to MNO SMSC
delivery_mode=2 persistence ensured
Web Channel Path
POST /api/sms/send → SMS API → RabbitMQ API Wrapper → Queue → Steps 5–8 identical to App/USSD
Async-first design: MNO back-pressure never reaches the transaction layer — Elma Core returns 202 before any SMS delivery attempt.

## Slide 6
Queue Naming & Routing Strategy
Granular isolation enables independent scaling, tuning, and fault containment
Queue Name Format:
{COUNTRY} _ {BANK_ID} _ {CATEGORY} _ SMS
Examples
UGANDA_99_OTP_SMS
Uganda · Bank 99 · One-Time Password
KENYA_12_PROMO_SMS
Kenya · Bank 12 · Promotional messages
TANZANIA_07_ALERT_SMS
Tanzania · Bank 7 · Account alerts
Operational Benefits
Independent Scaling
Per-segment throughput without cross-contamination
Priority Tuning
OTP: high prefetch · PROMO: low prefetch
Fault Isolation
Country outage does not affect other regions
Auditability
Queue depth reveals delivery delays per segment
Durability
durable:true + delivery_mode:2 — no message loss
Dead-letter queues capture all undeliverable messages — no silent failures.

## Slide 7
RabbitMQ & Queue Processors
Durable message bus with per-queue worker services
RabbitMQ Message Broker
Persistent storage
durable:true queues + delivery_mode:2 messages
Management UI/API
Real-time queue depth & throughput monitoring
AMQP protocol
Standard wire protocol for .NET consumers
Dead-letter routing
Failed messages auto-routed to DLQ
Horizontal scale
Clustering supported for HA deployments
Queue Processor Workers (×N)
One per queue
Dedicated .NET Worker Service container
Long-lived consumer
Single AMQP subscription — no polling overhead
HTTP 2xx → ACK
Message permanently removed from queue
HTTP 4xx → NACK
requeue=false → dead-letter queue
HTTP 5xx → NACK
requeue=true → retry up to limit → DLQ
Horizontal scaling
Multiple replicas share same queue (round-robin)

## Slide 8
SMS Splitter Gateway & MNO Delivery Layer
Intelligent routing from queue processor to mobile network operators
SMS Splitter Gateway
C# .NET · IIS (Windows Server)
• Receives HTTP POST from Queue Processors
• Extracts destination MSISDN from payload
• Longest-prefix match: +25677 → Airtel Uganda
• Forwards to resolved MNO Passthrough API URL
• Centralises routing table — one place to update MNO endpoints
• Per-MNO throughput logging & latency metrics
• Optional fallback to secondary MNO on failure
• Decouples processors from MNO-specific details
MNO Passthrough API + SMSC
Node.js · PM2 (Linux) — one instance per MNO
Passthrough API
• Accepts normalised HTTP SMS request
• Translates to MNO-specific protocol (SMPP / SDP)
• Submits to co-located SMSC module
• Returns delivery status to Splitter
SMSC Module (SMPP)
• Persistent TCP connection to MNO SMSC
• Manages bind/rebind, enquire_link keepalives
• Configurable window size & sequence tracking
• Exponential backoff rebind on session loss
SMSC Module (SDP)
• HTTP/HTTPS interface with auth & request signing
• Delivery receipts: correlates submit_sm_resp ACKs
• Processes deliver_sm receipts
• Supports SMPP 3.4 and SDP HTTP protocols
▶

## Slide 9
Deployment Topology
Three-tier infrastructure — Windows IIS · Docker · Linux PM2
Tier 1 — Windows Server (IIS)
▸ Elma Core (.NET API)
▸ SMS Splitter Gateway (.NET API)
Role: Transaction processing & MNO routing
Runtime: IIS on Windows Server
Scaling: Vertical or load-balanced
Tier 2 — Docker Host
▸ SMS API (C# container)
▸ RabbitMQ API Wrapper (C# container)
▸ Queue Processors A … N (Worker Svc containers)
▸ RabbitMQ Broker
Runtime: Docker (containerised)
Scaling: Horizontal container replicas
Tier 3 — Linux Server (PM2)
▸ MNO-A Passthrough + SMSC (Node.js)
▸ MNO-B Passthrough + SMSC (Node.js)
▸ MNO-N … (one process per MNO)
Runtime: PM2 process manager on Linux
Scaling: PM2 multi-instance per MNO
⟵ API calls ⟶
⟵ HTTP POST ⟶
All tiers are independently deployable. Tier 1 (IIS) handles business logic · Tier 2 (Docker) handles async messaging · Tier 3 (Linux/PM2) handles MNO protocol integration.

## Slide 10
Failure Modes & Resilience
Every failure scenario has a defined mitigation strategy
Failure
Impact
Mitigation
Severity
Elma Core unavailable
Transactions fail; no new SMS
Auto-restart + health-check
High
Queue API Wrapper down
Elma Core error; may retry internally
Container restart + Elma backoff
Med
RabbitMQ broker down
No new messages; existing safe on disk
Clustering + persistent disk storage
Med
Queue Processor crash
Messages unACKed, auto-requeued by broker
Auto-restart + consumer_timeout
Med
SMS Splitter Gateway down
5xx from processor → NACK & requeue
Backoff + dead-letter queue
Med
MNO Passthrough down
Delivery fails; propagates to processor
PM2 auto-restart + fallback MNO
Med
SMPP session lost
Delivery pauses until rebind
Exponential backoff rebind
Low
MNO network outage
SMSC-level failure
Dead-letter queue + scheduled retry
High
■ High risk ■ Medium risk ■ Low / Auto-recovered

## Slide 11
Non-Functional Characteristics
Throughput · Durability · Observability · Security
Throughput
• Queue Processor: bounded by SMS Splitter response time + prefetch count
• SMS Splitter Gateway: stateless HTTP handler — vertical scale or load balancer
• MNO Passthrough: bounded by SMPP window size (10–100 PDUs)
• PM2 supports multiple instances per MNO for higher throughput
• OTP queues: high prefetch · PROMO queues: low prefetch
Durability
• All RabbitMQ queues declared durable:true
• All messages sent with delivery_mode:2 (persisted to disk)
• Dead-letter queues prevent silent message loss
• SMPP persistent TCP with enquire_link keepalives
• Exponential backoff ensures no storm on reconnect
Observability
• Queue depth via RabbitMQ Management UI / API
• Delivery latency: timestamped at enqueue & SMSC ACK
• SMPP session health via enquire_link cycle monitoring
• Per-MNO throughput logging in SMS Splitter Gateway
• Dead-letter queue depth = unresolved delivery failures
Security & Ops
• TLS on all inter-service HTTP connections
• SMPP bind credentials per MNO (not shared)
• SDP HTTP auth & request signing per MNO
• Container isolation for queue processors
• IIS on Windows Server for Elma Core (enterprise hardened)

## Slide 12
Key Design Decisions
Architecture choices and the problems they solve
1. Async-First Delivery
Problem: MNO latency variability (50ms – 10s) would block transaction APIs.
Decision: Enqueue SMS immediately; return 202 Accepted to caller.
Benefit: Transaction layer never waits for carrier.
2. Queue-per-Segment
Problem: A slow MNO in one country was starving OTP delivery for another bank.
Decision: Isolate by COUNTRY × BANK_ID × CATEGORY.
Benefit: Fault containment; independent priority tuning.
3. Protocol Abstraction (Splitter + Passthrough)
Problem: Queue processors would need MNO-specific SMPP/SDP logic.
Decision: Two-layer gateway (Splitter routes, Passthrough adapts).
Benefit: New MNO integration = one new Passthrough instance, no processor changes.
4. Node.js for SMPP/SDP
Problem: .NET SMPP libraries lacked mature async keep-alive handling for African MNOs.
Decision: Node.js with event-loop for SMPP TCP persistence.
Benefit: Non-blocking SMPP window management; PM2 restart on crash.

## Slide 13
Glossary of Key Terms
AMQP
Advanced Message Queuing Protocol — RabbitMQ wire protocol
SMPP
Short Message Peer-to-Peer — binary protocol for SMSC submission
SMSC
Short Message Service Centre — MNO system for SMS storage/forwarding
SDP
Service Delivery Platform — HTTP/HTTPS SMS gateway
MNO
Mobile Network Operator — telecom carrier (MTN, Airtel, Safaricom …)
MSISDN
International mobile phone number (E.164 format)
OTP
One-Time Password — time-sensitive auth SMS category
PM2
Process Manager 2 for Node.js — keeps processes running, auto-restarts
IIS
Internet Information Services — Microsoft enterprise web server
DLQ
Dead-letter queue — holds failed messages for manual inspection/retry
Worker Service
Background .NET long-running service — no HTTP listener, just consumers
Prefetch count
Number of unACKed messages a consumer holds — RabbitMQ flow control
Window size
SMPP: max outstanding PDUs before awaiting acknowledgement
NACK
Negative acknowledgement — tells broker message was not processed

## Slide 14
ELMA
SMS Platform Architecture
Multi-Channel · Queue-Isolated · Protocol-Agnostic · Resilient
✓ Three entry channels (App, USSD, Web) converge on one async pipeline
✓ Granular queue isolation per Country × Bank × Category
✓ Async-first: MNO back-pressure never impacts transaction latency
✓ Dead-letter queues guarantee zero silent message loss
✓ Three-tier deployment: IIS · Docker · Linux/PM2 — independently scalable
Questions & Discussion
June 2026 · StayHere Engineering